## Slide 2
Troubleshooting Steps

## Slide 3
First Level Troubleshooting Steps
Step1: User needs to check whether mobile network is Available/ON or not. If not, please go to the settings tab and choose network manually and try to latch the network.
Step 2: User needs to check whether Data connection is ON/OFF, if ON move to Step 3
Step 3: User needs to go to the settings option & APN name needs to be changed as per the solution.
(APN Name for E.g. - abcbank.com)
Step 4: User needs to enter the username and password as per the solution provided to them. (Only for Static IPs)
Step 5: If User is using device in roaming scenario then roaming option should be ON at the device end.
Step 6: After performing above steps User should get E/H/VOLTE sign. If User is getting E/H/VOLTE sign, then connectivity is proper and User needs to check the reachability.
Step 7: User should try to reach whitelisted IPs/application as per the Solution
Step 8: If the User is still facing issue in reachability/connectivity then they can log a case with vbs.customerservice@Vodafoneidea.com
Users are requested to perform the following FLT steps before contacting CSD:

## Slide 4
Process flow for Ticket Booking
Step1: Customer will mark an email to Vbs.customerservice@vodafoneidea.com for ticket booking.
If customer have not shared the details which will require for ticket booking then associate will share the predesigned format with customer to share the required details.(Click here for Format)
Step 2: IOT associate will book the ticket on HPSM portal.
Step 3: Reply to customer with Incident ID(Sample ID: EN_IOT_31032022_732974). Share ticket details with customer along with the assuring time for initial observations within 60 mins.
Step 4: IOT executive will perform the basic checks in SCRM
If all checks are ok then go for ticket booking
If Number is suspended then route cases to Account Manager/Service Manager.
Step 5: Arrange call with customer for Live testing/troubleshooting

## Slide 5
Incidents reporting format
VI IoT/ M2M Issue Reporting (VBS.Customerservice@vodafoneidea.com) -24*7 | 
Toll Free Number:: 55666 or 9920055666 | 
Problem Statement | 
Issue Start Date | 
No of SIM Affected (Count) | 
Affected Sample Numbers (Mobile No/SIM No) (Sample Numbers for Bulk Attach over in Excel File ) | 
Sample Working Number If Any (Optional) | 
SPOC 1 Name & Contact Number for Troubleshooting/Testing | 
SPOC 2 Name & Contact Number | 
Device Level APN | 
Whitelisted IP/ URL's at device end & Port Numbers | 
Affected Number Location (Delhi, Mumbai, Bihar, Kolkata Etc.) | 
Type of SIM (e-SIM/ Standard) Optional | 
Type of Solution using in device (SMS/2G/3G/4G) | 
Any recent changes done (whitelisting/ APN change/ barring/ server change etc) | 
Account Manager Name (Optional) | 

## Slide 6
Data not working

## Slide 7
SCRM Pre Checks
Below are the basic checks for all data not working cases
Step 1 || Basic Checks in SCRM
If Operating Status should be active , If inactive, inform the Stakeholders and close the ticket
If Tariff Plan is non-IOT, inform the Stakeholders and close the ticket
If HLR Status is inactive, inform the Stakeholders and close the ticket
If APN is inactive, inform the Stakeholders and close the ticket
If Roaming is inactive, inform the Stakeholders and close the ticket
If GPRS is inactive, inform the Stakeholders and close the ticket
If Barring is active, inform the Stakeholders and close the ticket
Check the Data Balance
Check under sub component for any recent activities which leads to the outage
Device Level APN
From the incident reporting form shared by the customer, confirm that the APN configured in the device is same as configured in SCRM

## Slide 8
Step 2 || Compare the profile with working numbers
If customer have any working numbers, compare all the Step 1 with working numbers.
If any discrepancy with working numbers, inform the AM and Customer.
Step 3 || L1 Testing with the customer
If the issue is related to RF
If Customer deny doing the troubleshooting
If the number is Not Latched
If the Number is Latched and Data Not Working

## Slide 9
Scenario 1: If the customer device is working in one location and not working in other location
Scenario 2: Slow Speed/ Packet Drop/ Latency/ Data Buffering
Pre-requisite from Customer:
Get below table from customer and send to RF team for feedback
RF Issue Reporting | 
Problem Statement (RF Specific) | 
Impact Location & PIN Code | 
Latitude & Longitude of the impacted Location | 
RAT Technology Customer is facing the issue (2G/ 3G/ 4G) | 
End User Name & Contact Number | 
Signal Strength for (2G/ 3G/ 4G) at customer location, when checked in handset | 
G Net Track Snapshot | 
Send to RF SPOC for observation

## Slide 10
2. Customer deny doing the troubleshooting
Assign to B2X team for field visit and coordinate with customer and B2X for field visit and perform troubleshooting.
3. If the number is not latched
If SIM is newly activated SIM card, cross check the SIM number in SCRM and SIM Number from the back side of the SIM card.
Check If SIM Card is e-SIM
If Yes,
Send the numbers to the NILUSAGE/ EBO team for Service refresh
Ask customer to check the services post refresh. If numbers started working. Close the ticket.
Send the Numbers to the circle Switch Team for Purging
Ask customer to check the services post purging. If numbers started working. Close the ticket.
If No,
If SIM card is normal SIM card, ask customer to arrange device and handset for troubleshooting

## Slide 11
Perform Manual Latching. Ask the customer to insert SIM in a handset and select network operator as VI manually. If the latching is happening, then close the ticket.
Send the numbers to the NILUSAGE/ EBO team for Service refresh
Ask customer to check the services post refresh. If numbers started working. Close the ticket.
Send the Numbers to the circle Switch Team for Purging
Ask customer to check the services post purging. If numbers started working. Close the ticket.
If manual latching is not happening, ask AM & customer to perform SIMEX on Sample numbers
4. If the Number is latched and Data not working
Check SGSN & GGSN logs

## Slide 12
Step 4 || Identify the Solution
Data not working for public APN i.e. open internet
Raise the case with INM team
L2 Team:
INM @
DL-SNOC-PKC-INM-ZTE <DL-SNOC-PKC-INM-ZTE@vodafoneidea.com>;
DL-SNOC-PKC-INM-CISCO <DL-SNOC-PKC-INM-CISCO@vodafoneidea.com>;
DL-SNOC-PKC-INM-NOK <DL-SNOC-PKC-INM-NOK@vodafoneidea.com>;
DL-SNOC-PKC-INM-ERIC <DL-SNOC-PKC-INM-ERIC@vodafoneidea.com>;
DL-SNOC-PKC-INM-HUA <DL-SNOC-PKC-INM-HUA@vodafoneidea.com>
Data not working for the ISAFE
Compare the working and non-working numbers on the 6D portal

## Slide 13
Scenario 1: If APN is ISAFE/M2MISAFE- Check if number on 6D.
Number is not present on 6D
Inform the customer that numbers are not whitelisted and get in touch with AM and whitelist the numbers. Case closed
Number is present on 6D
Follow below steps to check further-
Check SIM in device and enable traces at SGSN & GGSN.
First check at SGSN and check whether getting create PDP request from the device towards the network.
If not ask to reboot the Device else reinsert SIM card wherever possible to reinitiate attach process from device
Attach request NOT received on network after reboot/reinserting the SIM
Proceed for manual latching if device have provision for manual latching if not ask to arrange any other device/data card/mobile handset(not necessary Android) for manual latching
Post manual latching reinsert the SIM in device and check if any hits are getting on network.
If not ask to involve device vendor
If yes Proceed for GGSN and SGSN logs

## Slide 14
Attach request received on network after reboot/reinserting the SIM
Proceed for GGSN and SGSN logs to check rejections
If rejections observed on SGSN check for the Cause values(page number to be Added) and work according to cause value.
If no rejections observed on SGSN proceed for GGSN logs.
Check if the hits are going on whitelisted IP/URL.
If hits are not on whitelisted IP/URL inform customer device requesting for non-whitelisted IP/URL check the device configuration and close the case from our end.
If hits are on the whitelisted IP/URL check if any redirections are there from the IP/URL.
For better understanding it is always recommended to use convert the GGSN trace in PCAP.
In case hits are on a whitelisted IP/URL and the user is not getting data on the same server confirmed from the server team Handover the case to L2.

## Slide 15
L2 Team:
SNOC @
Corsnoc M2miot (COR), Vodafone Idea <Corsnoc.M2MIOT@vodafoneidea.com>
Level | SPOC Name | Contact Number
Level 1 | Corsnoc.M2MIOT@vodafoneidea.com | 2071719563
Level 2 | Sidhartha.Jena4@vodafoneidea.com | 7666255316
Level 3 | Sanket.Deshpande@vodafoneidea.com | 7798984669
Level 4 | Vinodkumar.Barot@vodafoneidea.com | 8886500773
Level 4 | Sumant.singh2@vodafoneidea.com | 8411005972
Level 5 | Rashmin.shah@vodafoneidea.com | 9823003020
L2 Team Escalation Matrix

## Slide 16
Data not working Dynamic solution
Raise the case with L2
Raised the case with the RF if required (as per the L2 observation.)
Data not working - Static IP solution with AAA
Troubleshooting:
IP allocation handled by ECAAA server commonly called AAA team.
SIM configuration is done on the AAA server under the specific accounts which includes IMSI, MSISDN, IP Address, User name, Password.
After attach request accepted on the SGSN, IP allocation done via the AAA server on successful parameter checks during PDP activation
On successful authentication of requested parameters IP Allocation is done from AAA server
It is always a good practice to check AAA configuration with APPSINFRA Team to avoid unnecessary field visits/ customer dependency

## Slide 17
Depending upon the end user device type decide further way of troubleshooting.
Event Trace and/or GGSN trace can be used during FLT(prefer GGSN logs)
For devices with always ON nature(Modems) check the GGSN trace to check if any hits are observed
For devices with on demand connectivity(eg.- Data cards) connect with user and perform the general FLT
Incase any IP configuration issue observed during the testing request circle team to raise work order for configuration/reconfiguration
AAA mapping sheet from account manager
Validation of AAA with the AppsInfra.
Raise case with switch for profile / APN confirmation for dynamic IP assignment to the device.
Ping response & forward-reverse traceroute for working and non-working number to check with L2.
Check with the account manager for the NNI details i.e. MPLS circuit ID and PE-CE IP details.
Raise the case with L2
Group ID | <Enoc.AppsInfra@vodafoneidea.com>; | Contact No
L1 | rajesh.parvatani@wipro.com | 
L2 | naved.shaikh@wipro.com | 
L3 | AnilKumar Sonkawade (anilkumar.sonkawade@wipro.com) | 9168642641

## Slide 18
Data not working - Static IP solution with GDSP AAA
BASIC INFORMATION-
IP allocation handled on GDSP platform
SIM configuration done on GDSP platform against following details-
ICCID/SIM number, IMSI, IP address defined or requested by circle.
GDSP customer identifiers(Customer Name on GDSP,Customer ID,CSP ID)
Primary FLT-
SIM details validation on CRM along with Tariff plan.
Check IP allocation over GDSP in the affected SIM profile for IP details validation.
Connect SPOC for the primary FLT and keep the number on trace on GGSN/SGSN.
Handover the case to GDSP in agreed format if the issue persists post FLT.

## Slide 19
Basic checks in CRM
SGSN- GGSN observations
Basic checks in GDSP portal
Raise the case with GDSP
Raise the case with GDSP @ Corsnoc.Gdsp@vodafoneidea.com
Data not working -Static IP solution with HLR
BASIC INFORMATION-
IP allocation handled by HLR, all IPv6 configurations are by default on HLR/HSS
For Idea Static IP solution HLR/HSS IP configurations are done
SIM configuration is done on the HLR which includes IP allocation type (IPv4/IPv6), IP address, SIM Identifier (MSISDN/IMSI/ICCID) and RAT(2G/3G or 4G)
Primary FLT-
SIM details validation on CRM
Check IP configuration on HLR/HSS via circle switch team
Connect SPOC for FLT
Put the number on trace GGSN/SGSN for the logs and check if activate PDP request is received from the device
In case any issue persists post FLT involve switch team for the online testing with user.

## Slide 20
Packet drops/ Slow Speed/ Latency / Data buffering Issues

## Slide 21
Packet Drop Issue
Primary Checks
CRM checks(must check Data pack and balance)
Check the APN and Solution document for type of backhaul being used.
Refer solution document to check throttling is allowed
For shared APN proceed for the primary FLT.
Scenario 1: MPLS backhaul
Ask the customer to share at least 100 packets ping response and Traceroute from SIM to server and vice versa.
Check for the Signal strength available on the mobile handset for personal/M2M number
If weak coverage is observed proceed for the RF checks.
If traceroute is not complete check for the IP on which the RTO is observed depending upon the drops on MPLS network or RF network need to channelize the case to Fixed line support or RF team.
If everything looks good from a network perspective, ask the customer to check if SIM can be checked in any other device.

## Slide 22
Packet Drop Issue
Scenario 2: Internet backhaul
Check the RAT on which SIM card is latched.
Check for the Signal strength available on the mobile handset for personal/M2M number
In case any weak coverage is observed, channelize the case to the RF team for further checks.
If everything looks good from a network perspective, ask the customer to check if SIM can be checked in any other device.
Troubleshooting
Basic check in CRM.
Follow the RF checklist to check the network parameter
Ping response & forward-reverse traceroute for working and non-working number to check with L2

## Slide 23
Slow Speed / Latency Issue/ Data Buffering Issues
Primary Checks
CRM checks(must check Data pack and balance)
Check the APN and Solution document for type of backhaul being used.
Refer solution document to check throttling is allowed
For shared APN proceed for the primary FLT.
Scenario 1: MPLS backhaul
Ask the customer to share at least 100 packets ping response and Traceroute from SIM to server and vice versa.
Check for the average latency observed in the Ping response and ask the customer what is the expected latency.
Handover the case to L2 if high latency is observed.
Check for the Signal strength available on the mobile handset for personal/M2M number
If weak coverage is observed proceed for the RF checks
For 2G latched numbers ask the RF team to check the data channel availability at the affected site
Refer traceroute logs to check on which IP high latency is observed it will help to understand if an issue is in MPLS network or Radio network.
If latency is observed on last hop(Radio network) proceed for the RF checks
If latency is observed in hops other than last hop channelize the case to fixed lines for their end observations on the MPLS part.
If everything looks good from a network perspective, ask the customer to check if SIM can be checked in any other device and to share ping and trace response for the working number for reference.

## Slide 24
Slow Speed / Latency Issue/ Data Buffering Issues
Points be noted-
For 2G there is no minimal latency we can offer since 2G prefers voice traffic over Data.
Try to get the Gnet tracker/Network cell info lite screenshot for the VI SIM at the affected location
Scenario 2: Internet backhaul
Check the RAT on which SIM card is latched.
Check for the Signal strength available on the mobile handset for personal/M2M number
In case any weak coverage is observed, channelize the case to the RF team for further checks.
For 2G latched numbers, ask RF team to check the data channel availability at the affected site.
If everything looks good from a network perspective, ask the customer to check if SIM can be checked in any other device.

## Slide 25
SMS Issue

## Slide 26
P2P SMS Issue
Basic SMS Checks in CRM
MO & MT SMS
P2P SMS issue
Primary Checks-
Check the number if its Idea 13 digit number ask circle to remove the P2P whitelisting and configuration and close the case.
Incoming and outgoing SMS service must be active along with SMS camel flag.
Check if customer sending SMS through VI SIM if not ask to send SMS from whitelisted VI SIM card
Check for the P2P whitelisting details and cross check with the customer if the whitelisted source number is being used for sending SMS.
Ask customer to check sending SMS from other whitelisted numbers.

## Slide 27
P2P SMS issue
Check and confirm the SMSC Number configured on handset
  +919820005444(Vodafone) and +919702000555(Idea)
  Click on message app.
  Go to the setting.
  Click on additional settings
  Click on Short Message Service Centre(SMSC)
  Please check below note and enter SMSC number according to operator.
Ask customer for below details-
  SMS party A with current location
  SMS party B with current location
  Exact time stamp for the SMS send
  Error message and/or error screenshot
Raise the case with P2P and SMSC teams for the logs.
Analyse the logs received from both the teams and share the same with customer.
In case no hits received on the SMSC and P2P platform check with Switch team for the SMS related services checks.
GDSP SMS issue
Raise the case with GDSP @ Corsnoc.Gdsp@vodafoneidea.com

## Slide 28
NON P2P SMS issue
Non P2P SMS issue
Raise the case with VAS @ SNOC-ServiceDesk-VAS (COR), Vodafone Idea, COR-SNOC-L1-SDC; COR-SNOCVIL-MESSAGING; SNOC-ServiceDesk-VAS (COR), Vodafone Idea

## Slide 29
IOT Voice Call Issue

## Slide 30
Voice Call Issue
Step 1: Check the P2P whitelisting of Voice numbers Step 2: Check the numbers are Vodafone / Idea Numbers Step 3: Check camel flag for voice is active Step 4: Whitelist your number and try calling IOT number. Step 5: If call is not working as per solution, raise with Digi spice team with timestamp. Step 6: Follow Digi spice escalation matrix Step 7: If Digispice is not getting any hits check with home circle Switch team.
Digispice operation |  | 
 | Mail ID | Contact
Techops | techops@digispice.com | 9218514174
Level 1 : | pintu.chouhan@digispice.com | 9877623248
 | vijay.dhuriya@digispice.com | 7415443385
 | nitesh.gawade@digispice.com | 8108853039
Level 2 : | aditya.sharma@diigispice.com | 9219019090
Level 3 : | bijon.roy@digispice.com | 7042882755

## Slide 31: Thank you !