## Slide 1: SMS Flow Diagram and Troubleshooting

## Slide 2
Agenda
We will learn the flow of SMS services.
How is the troubleshooting done and which teams are involved in this process?

## Slide 3: Flow Diagram :
User 1 Party A/ Source Number
Prutech Platform
SMSC
10-digiti or 13-digit
Prutech checks the whitelisting of the number and also cross is the number valid or not
10-digit or 13-digit
User 2 Party B / Destination No.
It can be a Vi operator or another operator it is depend upon the user
Short Message Switching Center
Switch will Send a delivery Report to Sender and SMS will be received by the receiver
STP
Switch

## Slide 4: Troubleshooting of SMS Issue
Check the number if it’s an Idea 13-digit number ask Circle to remove the P2P whitelisting and configuration and close the case.
Incoming and outgoing SMS service must be active along with the SMS camel flag.
Check if the customer sending SMS through VI SIM if not ask to send SMS from a whitelisted VI SIM card
Check for the Prutech whitelisting details and cross-check with the customer if the whitelisted source number is being used for sending SMS.
Ask customers to check sending SMS from other whitelisted numbers.

## Slide 5: Troubleshooting of SMS Issue
Check and confirm the SMSC Number configured on the handset
  +919820005444(Vodafone) and +919702000555(Idea)
  Click on the message app.
  Go to the setting.
  Click on additional settings
  Click on Short Message Service Centre(SMSC)
  Please check the below note and enter the SMSC number according to an operator.
Ask the customer for the below details-
  SMS party A with the current location
  SMS party B with the current location
  Exact time stamp for the SMS send
  Error message and/or error screenshot
Raise the case with Prutech and SMSC teams for the logs.
Analyse the logs received from both teams and share the same with the customer.
In case no hits are received on the SMSC and P2P platform check with the Switch team for the SMS-related services checks.

## Slide 6: Thank You