## Slide 2
Troubleshooting Steps

## Slide 3
First Level Troubleshooting Steps
Step1: User needs to check whether mobile network is Available/ON or not. If not, please go to the settings tab and choose network manually and try to latch the network.
Step 2: User needs to check whether Data connection is ON/OFF, if ON move to Step 3
Step 3: User needs to go to the settings option & APN name needs to be changed as per the solution.
(APN Name for E.g. - abcbank.com)
Step 4: User needs to enter the username and password as per the solution provided to them. (Only for Static IPs)
Step 5: If User is using device in roaming scenario then roaming option should be ON at the device end.
Step 6: After performing above steps User should get E/H/VOLTE sign. If User is getting E/H/VOLTE sign, then connectivity is proper and User needs to check the reachability.
Step 7: User should try to reach whitelisted IPs/application as per the Solution
Step 8: If the User is still facing issue in reachability/connectivity then they can log a case with vbs.customerservice@Vodafoneidea.com
Users are requested to perform the following FLT steps before contacting CSD:

## Slide 4
Process flow for Ticket Booking
Step 1: Customer will send an email to Vbs.customerservice@vodafoneidea.com for ticket booking.
If a customer has not shared the details required for ticket booking then the associate will share the predesigned format with the customer to share the required details.
Step 2: The IoT associate will book the ticket on the HPSM portal.
Step 3: Reply to the customer with Incident ID(Sample ID: EN_IOT_01102024_732974). Share ticket details with the customer along with the assuring time for initial observations within 30 minutes.
Step 4: The IoT executive will perform the basic checks in SCRM/ Smart Central
If all checks are ok then go for ticket booking
If the Number is Suspended/Test in state then ask the customer to Activate the number with an Active deal.
Step 5: Arrange a call with the customer for Live testing/troubleshooting

## Slide 5
Incidents reporting format
VI IoT/ M2M Issue Reporting (VBS.Customerservice@vodafoneidea.com) -24*7 | 
Toll Free Number:: 55666 or 9920055666 | 
Problem Statement | 
Issue Start Date | 
No of SIM Affected (Count) | 
Affected Sample Numbers (Mobile No/SIM No) (Sample Numbers for Bulk Attach over in Excel File ) | 
Sample Working Number If Any (Optional) | 
SPOC 1 Name & Contact Number for Troubleshooting/Testing | 
SPOC 2 Name & Contact Number | 
Device Level APN | 
Whitelisted IP/ URL's at device end & Port Numbers | 
Affected Number Location (Delhi, Mumbai, Bihar, Kolkata Etc.) | 
Type of SIM (e-SIM/ Standard) Optional | 
Type of Solution using in device (SMS/2G/3G/4G) | 
Any recent changes done (whitelisting/ APN change/ barring/ server change etc) | 
Account Manager Name (Optional) | 

## Slide 6
Data not working

## Slide 7
SCRM Pre Checks
Below are the basic checks for all data not working cases
Step 1 || Basic Checks in SCRM
If Operating Status should be active, If inactive/ Suspended/ Test, inform the customer to active the number with the active deal and close the ticket
If the Tariff Plan is non-IOT, inform the Stakeholders and close the ticket
If HLR Status is inactive, forward to the 6d CMP team for activating the services.
If the APN is inactive, forward it to the 6d CMP team to activate the services.
If GPRS is inactive, forward to the 6d CMP team for activating the services.
If Barring is active, forward to the 6d CMP team for activating the services.
Check the Data Balance
Check under the orders section for any recent activities that lead to the outage
Device Level APN
From the incident reporting form shared by the customer, confirm that the APN configured in the device is the same as configured in SCRM/ Smart Central

## Slide 8
Step 2 || Compare the profile with working numbers
If a customer has any working numbers, compare all the Step 1 with working numbers.
Step 3 || L1 Testing with the customer
If the issue is related to RF
If Customer deny doing the troubleshooting
If the number is Not Latched
If the Number is Latched and Data Not Working

## Slide 9
Scenario 1: If the customer device is working in one location and not working in other location
Scenario 2: Slow Speed/ Packet Drop/ Latency/ Data Buffering
Pre-requisite from Customer:
Get below table from customer and send to RF team for feedback
Send to RF SPOC for observation
Sr. No | Mandatory Questionnaire | Feedback
1 | Customer/Account Details | 
2 | Address with land mark with location where customer facing issue | 
3 | Lat/Long of the location | 
4 | Nature of Issue | 
5 | Facing issues in which Network type(2G/3G/4G/VOLTE)* | 
6 | Device type in which SIM is used. | 
7 | Does the SIM work in normal handset | 
8 | Since how many days issue persisting | 
9 | Is the Issue At Any Specific hour of the day. If yes, specify | 
10 | Is Booster connected at the location and is it working | 
11 | Customer SPOC(End User/LC) | 

## Slide 10
Send to RF SPOC for observation
Unit Address | LAT | LONG | PLACE | 2G |  |  |  |  | 4G |  |  |  |  |  | Feedback | 2G/4G Optimization Possible or Not | POA
 |  |  |  | Serving Cell Name | LAC | RX quality | At onluRx level | 2G Idle Mode Cell ID | eNB | RSRP | TAC | SNR | SPEED DL (Mb/S | SPEED UL(Mb/S) |  |  | 
Please share the details in below format once the visit is done.

## Slide 11
2. Customer deny doing the troubleshooting
Assign to B2X team for field visit and coordinate with customer and B2X for field visit and perform troubleshooting.
3. If the number is not latched
If the SIM is a newly activated SIM card, cross-check the SIM number in SCRM and the SIM Number from the back side of the SIM card.
Check If the SIM Card is an e-SIM
If Yes,
Perform the purging activity once from the CMP portal
Ask customers to check the services post-purging. If numbers started working. Close the ticket.
Send the Numbers to the circle Switch Team for Purging for E-SIM
Ask the customer to check the services post-purging. If numbers started working. Close the ticket.
If No,
If the SIM card is normal, ask the customer to arrange the device and handset for troubleshooting

## Slide 12
Perform Manual Latching. Ask the customer to insert SIM in a handset and select network operator as VI manually. If the latching is happening, then close the ticket.
Perform the purging activity from CPM portal.
Ask customers to check the services post-purging. If numbers started working. Close the ticket.
If manual latching is not happening, ask AM & customer to perform SIMEX on Sample numbers
4. If the Number is latched and Data not working
Check SGSN & GGSN logs
Check the traces where getting hits on whitelisted IP/ Url or not.
Cross the P-Cap traces where is exact issue coming from the data communication.
If still the issue is not identified and data is not working forward this case to the concerned platform team like L2 SNOC, AAA(EC AA/A 6D CMP AAA), SANDVINE, or 6D ISAFE Team for further troubleshooting.

## Slide 13
Step 4 || Identify the Solution
Data not working for public APN i.e. open internet
Raise the case with INM team
L2 Team:
INM @
DL-SNOC-PKC-INM-ZTE <DL-SNOC-PKC-INM-ZTE@vodafoneidea.com>;
DL-SNOC-PKC-INM-CISCO <DL-SNOC-PKC-INM-CISCO@vodafoneidea.com>;
DL-SNOC-PKC-INM-NOK <DL-SNOC-PKC-INM-NOK@vodafoneidea.com>;
DL-SNOC-PKC-INM-ERIC <DL-SNOC-PKC-INM-ERIC@vodafoneidea.com>;
DL-SNOC-PKC-INM-HUA <DL-SNOC-PKC-INM-HUA@vodafoneidea.com>
Data not working for the ISAFE
Compare the working and non-working numbers on the 6D portal

## Slide 14
Scenario 1: If APN is ISAFE/M2MISAFE- Check if number on 6D.
Whitelisting on present on affected number
Inform the customer that numbers are not whitelisted and get the whitelisting done at your end from the portal. Case closed
Number is present on 6D
Follow the below steps to check further-
Check the SIM in the device and enable traces at SGSN & GGSN.
First check at SGSN and check whether creating a PDP request from the device towards the network.
If not ask to reboot the Device else reinsert the SIM card wherever possible to reinitiate the attach process from the device.
Attach request NOT received on network after reboot/reinserting the SIM
Proceed for manual latching if the device has provision for manual latching if not ask to arrange any other device/data card/mobile handset(not necessarily Android) for manual latching
Post manual latching reinsert the SIM in the device and check if any hits are getting on the network.
If not ask to involve the device vendor
If yes Proceed with GGSN and SGSN logs

## Slide 15
Attach request received on network after reboot/reinserting the SIM
Proceed for GGSN and SGSN logs to check rejections
If rejections are observed on SGSN check for the Cause values(page number to be Added) and work according to the cause value.
If no rejections are observed on SGSN proceed for GGSN logs.
Check if the hits are going on whitelisted IP/URL.
If hits are not on the whitelisted IP/URL inform the customer device requesting for non-whitelisted IP/URL check the device configuration, and whitelist the non-whitelisted IP/URL for testing purposes. After whitelisting still data is not working Kindly check with the 6D ISAFE Team.
If hits are on the whitelisted IP/URL check if any redirections are there from the IP/URL.
For better understanding it is always recommended to use convert the GGSN trace in PCAP.
In case hits are on a whitelisted IP/URL and the user is not getting data on the same server confirmed from the server team hand over the case to L2.

## Slide 16
L2 Team:
SNOC @
Corsnoc M2miot (COR), Vodafone Idea <Corsnoc.M2MIOT@vodafoneidea.com>
L2 Team Escalation Matrix
Level | Email Address | Name | Contact No.
Level 1 | Corsnoc.M2MIOT@vodafoneidea.com | SNOC DL ID | 020-7110-2454/ 2455
Level 2 | Sidhartha.Jena4@vodafoneidea.com | Siddhartha Jena | 7666255316
Level 3 | Deepak.Sharma6@vodafoneidea.com | Deepak Sharma | 8411000419
Level 4 | Gaurav.gupta10@vodafoneidea.com | Gaurav Gupta | 8411005387
Level 5 | Rajnish.khare@vodafoneidea.com | Rajnish Khare | 8411005495

## Slide 17
Data not working Dynamic solution
Raise the case with L2
Raised the case with the RF if required (as per the L2 observation.)
Data not working - Static IP solution with AAA
Troubleshooting:
IP allocation handled by EC AAA/ 6D CMP AAA server commonly called AAA team.
SIM configuration is done on the AAA server under the specific accounts which include IMSI, MSISDN, IP Address, User name, and Password.
After the attached request is accepted on the SGSN, IP allocation is done via the AAA server on successful parameter checks during PDP activation
On successful authentication of requested parameters IP Allocation is done from the AAA server
It is always a good practice to check AAA configuration with the AppsInfra Team to avoid unnecessary field visits/ customer dependency

## Slide 18
Depending upon the end user device type decide further way of troubleshooting.
Event Trace and/or GGSN trace can be used during FLT(prefer GGSN logs)
For devices with always ON nature(Modems) check the GGSN trace to check if any hits are observed
For devices with on demand connectivity(eg.- Data cards) connect with user and perform the general FLT
Incase any IP configuration issue observed during the testing request circle team to raise work order for configuration/reconfiguration
AAA mapping sheet from account manager
Validation of AAA with the AppsInfra.
Raise case with switch for profile / APN confirmation for dynamic IP assignment to the device.
Ping response & forward-reverse traceroute for working and non-working number to check with L2.
Check with the account manager for the NNI details i.e. MPLS circuit ID and PE-CE IP details.
Raise the case with L2
Group ID | <Enoc.AppsInfra@vodafoneidea.com>; | Contact No
L1 | enoc.appsinfra@vodafoneidea.com) | 020-42929311
L2 | kamal.paul1@wipro.com | 
L3 | AnilKumar Sonkawade (anilkumar.sonkawade@wipro.com) | 9168642641

## Slide 19
Packet drops/ Slow Speed/ Latency / Data buffering Issues

## Slide 20
Packet Drop Issue
Primary Checks
SCRM/ CMP checks(must check Data pack and balance)
Check the APN and Solution document for the type of backhaul being used.
Refer solution document to check throttling is allowed
For shared APN proceed for the primary FLT.
Scenario 1: MPLS backhaul
Ask the customer to share at least 100 packets ping response and Traceroute from SIM to server and vice versa.
Check for the Signal strength available on the mobile handset for personal/M2M number
If weak coverage is observed proceed for the RF checks.
If traceroute is not complete check for the IP on which the RTO is observed depending upon the drops on MPLS network or RF network need to channelize the case to Fixed line support or RF team.
If everything looks good from a network perspective, ask the customer to check if SIM can be checked in any other device.

## Slide 21
Packet Drop Issue
Scenario 2: Internet backhaul
Check the RAT on which SIM card is latched.
Check for the Signal strength available on the mobile handset for personal/M2M number
In case any weak coverage is observed, channelize the case to the RF team for further checks.
If everything looks good from a network perspective, ask the customer to check if SIM can be checked in any other device.
Troubleshooting
Basic check-in SCRM/ CMP
Follow the RF checklist to check the network parameter
Ping response & forward-reverse traceroute for working and non-working numbers to check with L2

## Slide 22
Slow Speed / Latency Issue/ Data Buffering Issues
Primary Checks
CRM checks(must check Data pack and balance)
Check the APN and Solution document for type of backhaul being used.
Refer solution document to check throttling is allowed
For shared APN proceed for the primary FLT.
Scenario 1: MPLS backhaul
Ask the customer to share at least 100 packets ping response and Traceroute from SIM to server and vice versa.
Check for the average latency observed in the Ping response and ask the customer what is the expected latency.
Handover the case to L2 if high latency is observed.
Check for the Signal strength available on the mobile handset for personal/M2M number
If weak coverage is observed proceed for the RF checks
For 2G latched numbers ask the RF team to check the data channel availability at the affected site
Refer traceroute logs to check on which IP high latency is observed it will help to understand if an issue is in MPLS network or Radio network.
If latency is observed on last hop(Radio network) proceed for the RF checks
If latency is observed in hops other than last hop channelize the case to fixed lines for their end observations on the MPLS part.
If everything looks good from a network perspective, ask the customer to check if SIM can be checked in any other device and to share ping and trace response for the working number for reference.

## Slide 23
Slow Speed / Latency Issue/ Data Buffering Issues
Points be noted-
For 2G there is no minimal latency we can offer since 2G prefers voice traffic over Data.
Try to get the Gnet tracker/Network cell info lite screenshot for the VI SIM at the affected location
Scenario 2: Internet backhaul
Check the RAT on which SIM card is latched.
Check for the Signal strength available on the mobile handset for personal/M2M number
In case any weak coverage is observed, channelize the case to the RF team for further checks.
For 2G latched numbers, ask RF team to check the data channel availability at the affected site.
If everything looks good from a network perspective, ask the customer to check if SIM can be checked in any other device.

## Slide 24
SMS Issue

## Slide 25
P2P SMS Issue
Basic SMS Checks in CRM
MO & MT SMS
Prutech SMS issue
Primary Checks-
Check the number if it’s Idea 13-digit number ask Circle to remove the P2P whitelisting and configuration and close the case.
Incoming and outgoing SMS service must be active along with the SMS camel flag.
Check if the customer sending SMS through VI SIM if not ask to send SMS from a whitelisted VI SIM card
Check for the Prutech whitelisting details and cross-check with the customer if the whitelisted source number is being used for sending SMS.
Ask customers to check sending SMS from other whitelisted numbers.

## Slide 26
P2P SMS issue
Check and confirm the SMSC Number configured on the handset
  +919820005444(Vodafone) and +919702000555(Idea)
  Click on the message app.
  Go to the setting.
  Click on additional settings
  Click on Short Message Service Centre(SMSC)
  Please check the below note and enter the SMSC number according to an operator.
Ask the customer for the below details-
  SMS party A with the current location
  SMS party B with the current location
  Exact time stamp for the SMS send
  Error message and/or error screenshot
Raise the case with Prutech and SMSC teams for the logs.
Analyse the logs received from both teams and share the same with the customer.
In case no hits are received on the SMSC and P2P platform check with the Switch team for the SMS-related services checks.

## Slide 27
IOT Voice Call Issue

## Slide 28
Voice Call Issue
Step 1: Check the P2P whitelisting of Voice numbers Step 2: Check the numbers are Vodafone / Idea Numbers Step 3: Check camel flag for voice is active Step 4: Whitelist your number and try calling the IOT number. Step 5: If the call is not working as per the solution, raise it with the Prutech team and Switch with a timestamp. Step 6: Follow Digi spice escalation matrix Step 7: If Digispice is not getting any hits check with the home circle Switch team.
Escalation Matrix P2P support |  |  |  | 
Level | Designation | Name | Email | Phone
1 | Customer complaint support | Service Experience Team | serviceexperience@prutech.in | 9846002138
 | IT & Network support | Jijo | jijot@prutech.in | 9846068623
2 | Operation Head | AV Thomas | avthomas@prutech.co.in | 9995019907
 |  | Manjusha M Bhat | manjusha@prutech.co.in | 8089455368
3 | IT & Network Head | Vijesh M V | vijesh@prutech.in | 9847724201
4 | HOD– Service Operations | Suraj P | suraj@prutech.co.in | 9847712093

## Slide 29: Thank you !